## Slide 1: Chapter 1 Computer System Overview
Ninth Edition
By William Stallings
Operating Systems: Internals and Design Principles
Notes: “Operating Systems: Internal and Design Principles”, 9/e, by William Stallings, Chapter 1 “Computer System Overview”.

## Slide 2: Operating System
Exploits the hardware resources of one or more processors
Provides a set of services to system users
Manages secondary memory and I/O devices

## Slide 3: Basic Elements
Processor
Main Memory
I/O Modules
System Bus

## Slide 4: Processor
Controls the operation of the computer
Performs the data processing functions
Referred to as the Central Processing Unit (CPU)

## Slide 5: Main Memory
Stores data and programs
Typically volatile
  Contents of the memory is lost when the computer is shut down
Referred to as real memory or primary memory

## Slide 6: I/O Modules
Move data between the computer and its external environment
Secondary memory devices (e.g. disks)
Communications equipment
Terminals

## Slide 7: System Bus
  Provides for communication among processors, main memory, and I/O modules

## Slide 9: Microprocessor
  Invention that brought about desktop and handheld computing
  Contains a processor on a single chip
  Fastest general purpose processors
  Multiprocessors
  Each chip (socket) contains multiple processors (cores)

## Slide 10: Graphical Processing Units (GPU’s)
  Provide efficient computation on arrays of data using Single-Instruction Multiple Data (SIMD) techniques pioneered in supercomputers
  No longer used just for rendering advanced graphics
    Also used for general numerical processing
        Physics simulations for games
        Computations on large spreadsheets

## Slide 11: Digital Signal Processors (DSPs)
  Deal with streaming signals such as audio or video
  Used to be embedded in I/O devices like modems
      Are now becoming first-class computational devices, especially in handhelds
  Encoding/decoding speech and video (codecs)
  Provide support for encryption and security

## Slide 12: System on a Chip (SoC)
To satisfy the requirements of handheld devices, the classic microprocessor is giving way to the SoC
    Other components of the system, such as DSPs, GPUs, I/O devices (such as codecs and radios) and main memory, in addition to the CPUs and caches, are on the same chip

## Slide 13: Instruction Execution
A program consists of a set of instructions stored in memory
Processor reads (fetches) instructions from memory
Processor executes each instruction
Two steps

## Slide 15: Instruction Fetch and Execute
The processor fetches an instruction from memory
Typically the program counter (PC) holds the address of the next instruction to be fetched
      PC is incremented after each fetch

## Slide 16: Instruction Register (IR)
Fetched instruction is loaded into Instruction Register (IR)
Processor interprets the instruction and performs required action:
      Processor-memory
      Processor-I/O
      Data processing
      Control

## Slide 19: Interrupts
Mechanism by which other modules may interrupt the normal sequencing of the processor
Provided to improve processor utilization
    Most I/O devices are slower than the processor
    Processor must pause to wait for device
    Wasteful use of the processor

## Slide 20
Table 1.1 Classes of Interrupts
Program Generated by some condition that occurs as a result of an instruction execution, such as arithmetic overflow, division by zero, attempt to execute an illegal machine instruction, and reference outside a user's allowed memory space.
Timer Generated by a timer within the processor. This allows the operating system to perform certain functions on a regular basis.
I/O Generated by an I/O controller, to signal normal completion of an operation or to signal a variety of error conditions.
Hardware Generated by a failure, such as power failure or memory
failure parity error.

## Slide 21: Figure 1.5a Flow of Control Without Interrupts

## Slide 22
Figure 1.5b
Short I/O Wait
X = interrupt occurs during course of execution of user program

## Slide 23
Figure 1.5c
Long I/O Wait

## Slide 30: Multiple Interrupts
An interrupt occurs while another interrupt is being processed
e.g. receiving data from a communications line and printing results at the same time
Two approaches:
Disable interrupts while an interrupt is being processed
Use a priority scheme

## Slide 33: Memory Hierarchy
Design constraints on a computer’s memory
    How much?
    How fast?
    How expensive?
If the capacity is there, applications will likely be developed to use it
Memory must be able to keep up with the processor
Cost of memory must be reasonable in relationship to the other components

## Slide 34: Memory Relationships
Faster access time = greater cost per bit
Greater capacity = smaller cost per bit
Greater capacity = slower access speed

## Slide 35: The Memory Hierarchy
Going down the hierarchy:
  Decreasing cost per bit
  Increasing capacity
  Increasing access time
  Decreasing frequency of access to the memory by the processor

## Slide 37: Principle of Locality
Memory references by the processor tend to cluster
Data is organized so that the percentage of accesses to each successively lower level is substantially less than that of the level above
Can be applied across more than two levels of memory

## Slide 38
Secondary Memory
Also referred to as auxiliary memory
External
Nonvolatile
Used to store program and data files

## Slide 39: Cache Memory
Invisible to the OS
Interacts with other memory management hardware
Processor must access memory at least once per instruction cycle
Processor execution is limited by memory cycle time
Exploit the principle of locality with a small, fast memory

## Slide 43: Cache Design
Main categories are:
Cache size
Block size
Mapping function
Write policy
Number of cache levels
Replacement algorithm

## Slide 44: Cache and Block Size
Cache Size
Small caches have significant impact on performance
Block Size
The unit of data exchanged between cache and main memory

## Slide 45: Mapping Function
Two constraints affect design:
When one block is read in, another may have to be replaced
The more flexible the mapping function, the more complex is the circuitry required to search the cache
Determines which cache location the block will occupy

## Slide 46: Replacement Algorithm
Chooses which block to replace when a new block is to be loaded into the cache
  Least Recently Used (LRU) Algorithm
  Effective strategy is to replace a block that has been in the cache the longest with no references to it
  Hardware mechanisms are needed to identify the least recently used block

## Slide 47: Write Policy
Dictates when the memory write operation takes place
Can occur every time the block is updated
Can occur when the block is replaced
Minimizes write operations
Leaves main memory in an obsolete state

## Slide 48: I/O Techniques
Three techniques are possible for I/O operations:
Programmed I/O
Interrupt-Driven I/O
Direct Memory Access (DMA)
When the processor encounters an instruction relating to I/O, it executes that instruction by issuing a command to the appropriate I/O module

## Slide 49: Programmed I/O
The I/O module performs the requested action then sets the appropriate bits in the I/O status register
The processor periodically checks the status of the I/O module until it determines the instruction is complete
With programmed I/O the performance level of the entire system is severely degraded

## Slide 50: Interrupt-Driven I/O
Processor issues an I/O command to a module and then goes on to do some other useful work
The processor executes the data transfer and then resumes its former processing
The I/O module will then interrupt the processor to request service when it is ready to exchange data with the processor
More efficient than Programmed I/O but still requires active intervention of the processor to transfer data between memory and an I/O module

## Slide 51: Interrupt-Driven I/O Drawbacks
Transfer rate is limited by the speed with which the processor can test and service a device
The processor is tied up in managing an I/O transfer
      A number of instructions must be executed for each I/O transfer

## Slide 52: Direct Memory Access (DMA)
When the processor wishes to read or write data it issues a command to the DMA module containing:
Whether a read or write is requested
The address of the I/O device involved
The starting location in memory to read/write
The number of words to be read/written
Performed by a separate module on the system bus or incorporated into an I/O module

## Slide 53: Direct Memory Access
Transfers the entire block of data directly to and from memory without going through the processor
    Processor is involved only at the beginning and end of the transfer
    Processor executes more slowly during a transfer when processor access to the bus is required
More efficient than interrupt-driven or programmed I/O

## Slide 54: Symmetric Multiprocessors (SMP)
A stand-alone computer system with the following characteristics:
  Two or more similar processors of comparable capability
  Processors share the same main memory and are interconnected by a bus or other internal connection scheme
  Processors share access to I/O devices
  All processors can perform the same functions
  The system is controlled by an integrated operating system that provides interaction between processors and their programs at the job, task, file, and data element levels

## Slide 55: SMP Advantages
Performance
A system with multiple processors will yield greater performance if work can be done in parallel
Availability
The failure of a single processor does not halt the machine
Incremental Growth
An additional processor can be added to enhance performance
Scaling
Vendors can offer a range of products with different price and performance characteristics

## Slide 57: Multicore Computer
Also known as a chip multiprocessor
Combines two or more processors (cores) on a single piece of silicon (die)
    Each core consists of all of the components of an independent processor
In addition, multicore chips also include L2 cache and in some cases L3 cache

## Slide 59: Summary
Cache memory
    Motivation
    Cache principles
    Cache design
Direct memory access
Multiprocessor and multicore organization
    Symmetric multiprocessors
    Multicore computers
Basic Elements
Evolution of the microprocessor
Instruction execution
Interrupts
    Interrupts and the instruction cycle
    Interrupt processing
    Multiple interrupts
The memory hierarchy
Notes: Summary of Chapter 1.